## Slide 1: Basic PIC-C I2C Communication
Arnan (Roger) Sipitakiat
Department of Computer Engineering, Chiang Mai University, Thailand

## Slide 2: I2C Basics
I2C is a Bus. Serial is point-to-point
Master and Slave pair
  Master must start the communication
  Slave can only respond
Slave has a 8-bit address
  Bit 0 is reserved for direction control

## Slide 3: Basic I2C Bus Setup
MASTER
SLAVE 1
SLAVE 2
5V
Pull-up Resistors
SCL
SDA

## Slide 4: i2C Commands in PIC-C
Master Only
  I2c_start()
  I2c_stop()
Slave Only
  I2c_isr_state()
Master & Slave
  I2c_read()
  I2c_write()

## Slide 5: Sending 1 Byte to Slave
I2c_start()
I2c_write(slave addr | 0)
I2c_write(registerAddress)
I2c_write(value)
I2c_stop()
MASTER
SLAVE
Address | Content
0 | 0
1 | 0
2 | 0
3 | 0
4 | 0
5 | 0
6 | 0
7 | 0

## Slide 6: Reading 2 bytes from slave
I2c_start()
I2c_write(slave addr | 0)
I2c_write(registerAddress)
I2c_start()
I2c_write(slave addr | 1)
Value1 = I2c_read()
Value2 = I2c_read(0)
I2c_stop()
MASTER
SLAVE
Address | Content
0 | 0
1 | 0
2 | 0
3 | 0
4 | 0
5 | 0
6 | 0
7 | 0

## Slide 7: Write ค่า 50 ไปยัง Register 5 ของ slave ที่มี address = 100
I2c_start();
I2c_write(100 | 0);
I2c_write(5);
I2c_write(50);
I2c_stop();

## Slide 8: Write ค่า 1000 ไปยัง Register 5 (ไบท์บน), 6 (ไบท์ล่าง) ของ slave ที่มี address = 100
I2c_start();
I2c_write(100 |0);
I2c_write(5);
I2c_write(1000 >> 8); // upper byte of 1000
I2c_write(1000 & 0xFF); // lower byte of 1000
I2c_stop();

## Slide 9: Read ค่าจาก Register 5 ของ slave ที่มี address = 100
Int returnValue;
I2c_start();
i2c_write(100 |0);
I2c_write(5);
I2c_start();
I2c_write(100 | 1);
returnValue = i2c_read(0);
I2c_stop();

## Slide 10: Read ค่าเซ็นเซอร์ 2 byte จาก Register 5,6 ของ slave ที่มี address = 100
Int v1,v2;
I2c_start();
i2c_write(100 |0);
I2c_write(5);
I2c_start();
I2c_write(100 | 1);
v1 = i2c_read();
V2 = i2c_read(0);
I2c_stop();

## Slide 11: Example I Controlling the Display Module Address = 0xB0
Register Address | Function
2 | High Byte
3 | Low Byte

## Slide 12: Example Program
// i2c1 - Master
#use i2c(MASTER, I2C1)
// Show the number 100 on the screen
I2c_start();
I2c_write(0xB0 | 0); // display module address
I2c_write(2); // show number command
I2c_write(0);
I2c_wirte(100);
I2c_stop();

## Slide 13: Example II Reading from the ultrasonic sensor

## Slide 14: How the module works

## Slide 15: Direct Connection to the module You need to do all the timing yourself
Implement timing

## Slide 16
I2C
Take care
of timing
Offload to an I2C Host
Let an I2C host perform the timing

## Slide 17: Tradeoffs of offloading
The Good
  The sensor is simpler to use.
  The main processor is free to do other things.
  More modular.
The Bad
  More expensive
  Must be careful of timing problems on the I2C host

## Slide 18: Example 3: I2C devices on the market
Digital Clock
Barometer
Temperature & RH
Color Sensor
Accelerometer
Motor Driver

## Slide 19: Motor Driver Module
Register Address | Function
0x82 | Speed (0-255)
0x84 | PWM Frequency
0xAA | Direction (0/1)
0xA1 | Select Motor A (0/1)
0xA5 | Select Motor B (0/1)

## Slide 20: Clock Module Module address = 0xD0